## Slide 1: Presentation 14th February
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
Chemical Engineering
Design Projects 4
Red Planet Recycle
An Investigation Into Advanced Life Support system for Mars
Tuesday 14th January, 2 PM

## Slide 2: Urine Processing Assembly (UPA)
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
Gareth Herron
14/02/2012

## Slide 3: Block Flow Diagram
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
1
2
3
4
5
6
7
8

## Slide 4: BFD Legend
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment

## Slide 5: Block Flow Diagram
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
1
2
3
4
5
6
7
8

## Slide 6: Point 1 – Urine Inlet
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
Composition of urine entering system:
Each crew member produces 2kg/day
This results in 20kg/day for the whole 10 man crew

## Slide 7: Block Flow Diagram
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
1
2
3
4
5
6
7
8

## Slide 8: Point 2 - Pretreatment
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
Components used in pre-treatment:
  Chromium Trioxide acts as a germicide and an oxidant
  Copper sulphate prevents mold forming
  Sulphuric acid is used to fix ammonia which would otherwise be dissolved
Composition of pre-treatment solution:
1 litre of urine is treated with 4 ml of this aqueous solution

## Slide 9: Why Vapour Compression Distillation?
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
Designed to mechanically mimic the earth’s natural cycle
Energy efficiency is one of the major plus points of the VCD system
  VCD reuses heat from the condensation process to reheat the inlet feed
Pending a requested paper for further analysis

## Slide 10
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment

## Slide 11: Mostly Liquid Separator and Particulate Filter
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
The mostly liquid Separator is designed to remove free gas that has trapped in the waste water tank such as excess air
–most likely be a pressure driven vertical gas-liquid separator with a demister for a high efficiency and to enable a smaller design
The Particulate filter is designed to remove free solids such as hair before they enter the multi-filtration beds
– gravity or pressure driven filtration or the use of hydro-cyclones which are able to remove solid particles without the use of filtration.
To be determined this week

## Slide 12
Design of Multi-Filtration Beds The following table summaries the amount of Empty Bed Contact Time, along with the amount of kilograms that will pass in the allocated time based on the flow rate of 200.6kg/day. The Volume in m3 was then determined.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment

## Slide 13
Multi-Filtration Beds
The following Table of Dimensions was then designed based on the volume of each individual component making up the multi filtration unit
A standard Length and Breadth of 0.2m by 0.1 m was used and thus the height was determined.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment

## Slide 14: Gas-Liquid Separator
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
.
g
For the removal of excess Oxygen from the Reactor’s exit stream, two gas – liquid separation units are compared:
Gas-Liquid Cyclone Separator is a better selection as vertical separators rely on gravity which is not as high in mars and in order to be efficient centrifugal force needs to be utilised such as the case of the cyclone separator
Separator | Advantages | Disadvantages
Vertical Separator | Simple Process design and can be a small design due to the use of a de-entrainment pad | If Inlet stream momentarily becomes overpowering it can fail. Common liquid separator won’t function on lower gravity field
Gas- liquid Cyclone Separator | Highly efficient and can operate in lower gravity environment’s | Lack of data for exact efficiencies

## Slide 15: Membrane bioreactor
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
Feedback from Lester taken on to next stage of design
Risk assessment is required
Aim:
Identify possible risk of failures and key dependencies
Simulate a working back-up for each stage, increasing reliability for the entire process

## Slide 16
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment

## Slide 17: Categorising risk
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
Which area of design is most likely to fail?
Which failure is most critical to operation ?
Least likely to fail
Temp & PH control
Chemical loss
Contamination
Membrane
Pumps
Backwash
Aeration
UV exposure
Critical failure
Critical failure

## Slide 18: Air Treatment
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment

## Slide 19: Air Filtration and Trace Contaminant Removal System
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment
Both separate systems from the air recycle system.
Air Filtration – to remove particulates such as microbes etc.
Trace Contaminant Removal – to remove potentially harmful chemicals that may build up during air recycle.

## Slide 20: Air Filtration
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment
HEPA (High Efficiency Particulate Air) Filter
  To qualify as HEPA by government standards, an air filter must remove 99.97% of all particles greater than 0.3 micrometer from the air.
  Trap bacteria, viruses and other particulates.
  Filter needs replacing every 3-4 years.
  Can incorporate a high energy UV light unit to kill off live bacteria and viruses trapped in filter.

## Slide 21: Trace Contaminant Removal
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment
Carbon Bed – for removing high molecular weight compounds. On ISS bed needs replacing every 90 days.
Catalytic Oxidiser – to convert CO, CH4, H2 and other low molecular weight compounds that are not absorbed by the charcoal bed to CO2 and H2O.
Sorbent bed – removes the undesirable acidic by products of catalytic oxidation such as HCl, Cl2, F2, NO2, and SO2.

## Slide 22: CO2 Separation
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment

## Slide 23: Desiccant Bed
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment
To remove remaining water vapour from air.
Desiccant subsystem consists of two beds, one adsorbs while the other desorbs.
Process gas flow drawn from cabin into adsorbing desiccant bed.
Alternating layers of zeolite 13X and silica gel in order to protect the silica gel from entrained water droplets which may cause the silica gel to swell and fracture.
Perforated metal screens and fibre filters in place at each end to stop desiccant particles and dust entering the gas stream.
Wet Air
Dry Air
Zeolite 13X
Silica Gel
Perforated metal screens and fibre filters

## Slide 24: Desiccant Bed
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment
Inlet Temperature – 20˚C
Relative Humidity – 50%
  Maintained by dehumidifier
From psychrometric graph:
  Dew point temperature – 9.4˚C
Need
  Silica gel adsorption capacity
  Time for regeneration

## Slide 25: Pre-cooling
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment
Almost all water has been removed in the desiccant bed (dew point of -62DegC)
Fluid stream must now be cooled to allow for more efficient adsorption

## Slide 26: Isosteric Heat of Adsorption
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment
A plot can be made of lnP versus reciprocal absolute temperature for various loadings.
Taking the CO2 loading as around 12g/100g sorbent, the slope of the line can be plotted on a loading versus heat of adsorption graph.
Isosteric heat of adsorption will be roughly 30kj/mol

## Slide 27: Zeolite 5A Adsorbent Bed
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment
Stream then enters the adsorbent bed
After a time, solid near the inlet becomes saturated
Majority of mass transfer takes place further and further from the inlet as time goes on
Once the exit CO2 concentration reaches C/Co > 0.05, the flow is diverted to the second bed
Since only the very last portion of exit fluid has such a high concentration, the average fraction of solute removed is often 0.99 or higher.

## Slide 28: Efficient Mass Transfer
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment
In order to utilise as much of the bed as possible, a narrow mass transfer zone (in proportion to bed length) is desired, and which is dependant upon:
  Mass transfer rate
  Fluid flow rate
  Shape of the equilibrium curve

## Slide 29: Regeneration
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment
Once the bed is offline, it will be heated to 204DegC, the heat of desorption for CO2.
A vacuum will be applied to the bed, with desorbed CO2 removed into a CO2 holding vessel.
Once all CO2 is desorbed, the bed must be cooled back to its original temperature.

## Slide 30: Cycle Times
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment
In order to make the design as efficient as possible, there should be little or no holding time in between adsorption cycles.
Regeneration time should be almost equal to adsorption time. (ta = th + tc)
Typical values for th and tc are 0.66 and 0.33.
Shorter cycle times will allow for smaller beds and CO2 holding vessels.
Each bed is regenerated several times a day on the ISS – possibly giving a ta of roughly 2 or 3 hours.

## Slide 31: Redundancy by Duplication
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment
All papers on the subject advise accounting for:
  Loss of capacity
  Attrition
  Some poisoning of the bed
Should a third bed be installed to allow for maintenance/flushing?
.

## Slide 32: CO2 Treatment
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment

## Slide 33: Sabatier Reactor
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment

## Slide 34: Rate equation used to model
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment
Proposed by Lunde (1974) for Sabatier reaction on ruthenium-alumina catalyst. Used to model reaction for reactor development since.

## Slide 35: Heat generation
Also proposed by Lunde (1974), used in conjunction with heat capacity of the gas stream to give the change in temperature through the reactor.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment

## Slide 36: Isothermal vs non-isothermal performance
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment

## Slide 37: Considerations given to air and water purity
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment
Air Purity
HEPA Filters
Activated carbon filters
UV exposure
Water from Sabatier will have low concentrations of dissolved CO2 ,methane and hydrogen following condensation of steam. CO2 will react with KOH electrolyte and form K2CO3 and water. Methane is relatively insoluble in water and so would not cause issues with the system. Hydrogen gas would most likely separate from the liquid mixture due to its low density.

## Slide 38: Solubility of gases in water
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment

## Slide 39
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment
Using the maximum solubility's from the previous diagram we can estimate that for our production of ~ 8kg/day of water the dissolved gas content will be methane - 0.032 g, hydrogen - 0.0152g and Carbon dioxide – 28 g

## Slide 40: Electrolysis Unit Design
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment

## Slide 41: Design Basis
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment
Rate of Oxygen Production = 8.4 kg/day
Rate of Hydrogen Production = 1.05 kg/day
Rate of Water consumption = 9.45kg/day
Fully detailed design is beyond the scope of this project
Key parameters have been calculated and additional parameters obtained from commercial examples

## Slide 42: Key Design Parameters
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment
Electrolysis Selection
Electrode Material
Diaphragm Material
Electrolyte Selection
Current Requirement
Minimum Voltage Requirement
Electrode Surface Area Requirement

## Slide 43: Qualitative Design
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment
Electrolysis Selection – Bipolar Electrolysis
Electrode Material – Platinum
Diaphragm Material – Sintered Nickel
Electrolyte – 30%wt KOH

## Slide 44: Quantitative Design
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment
Current Calculation
Required Current = 1.17kA

## Slide 45: Quantitative Design
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment
Minimum Voltage Calculation
Minimum Voltage Requirement = 1.10V

## Slide 46: Quantitative Design
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment
Electrode Area dependant upon Electrode Current Density
Typically found by experiment as it is dependant upon electrolyte concentration, temperature and pressure.
Struggling to find a value so far

## Slide 47: Scaled Commercial Data
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment
Operating Temperature = 40degC
Operating Pressure = 11bara
Electrolyte is coolant with design Tmax of 40degC.
Coolant(Electrolyte) Flowrate = 20.738kg/hr
Split between the product streams = 10.369 kg/hr each
http://www.hydrogenics.com/assets/pdfs/Industrial%20brochure_English.pdf

## Slide 48: Exit Stream Composition
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment

## Slide 49: Gas-Liquid Separation
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment
Gravity – System is operating under low gravity
2. Distillation – Similar to gravity system, not suitable to
gas-liquid separation.
Adsorption – Complex adsorption/desorption process,
adsorbents decrease the water purity.
Membrane – The size of the molecule of water is bigger
than the size of gas’ molecule

## Slide 50: Centrifugal Separator
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment
Centrifugal separator is the best choice for separate oxygen or hydrogen bubble from electrolyte flow
Centrifugal separation occurs when a mixture in the machine's chamber is spun very quickly, and heavy materials (in this case, electrolyte) typically settle differently than lighter ones (bubble).
Electrolyte is then typically collected from the bottom and bubble can be collected, as it rises to the top and through an exit opening in the centrifugal separator

## Slide 51: Separator Design Basis
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment
Assumptions:
All bubbles in liquid phase are evenly distributed
The density of liquid phase is uniform
Gas-Liquid mixture make a rotary motions with the same velocity in the centrifugal chamber
Neglect the action of gravity, only consider centrifugal force during the separation process.

## Slide 52: GAS-LIQUID CYLINDRICAL CYCLONE
.
Outline
1. Design
objectives
2. Criteria & constraints
3. Stages
1&2 Outline
4. Water
treatment
5. Air
treatment